## Slide 1: Wireless Broadband 101:
Technologies, capabilities and potential use cases

## Slide 2: A Public Utility Consortium Serving Washington State with Broadband and Next Generation 911 Services
How the Northwest connects
Greg Berry
Senior Network Design Engineer
Sean Ogden
Wireless Design Engineer

## Slide 3: What is Wireless Communication?
TRANSMISSION OF INFORMATION USING RADIO WAVES
  Two-Way Radio (Transmit and Receive)
    Walkie Talkie
    Bluetooth
    Wi-Fi
    Cellular Networks
    Satellite

## Slide 4: How does it work?
RADIO FUNDAMENTALS
  Different Radios for different jobs (Throughput, Range, Environment)
    Bluetooth – 30 feet, low bandwidth
    Wi-Fi – 50 yards, 1Gbps+
    Cellular (4G/5G) – A few blocks to ~10 miles, 1Gbps+
    PtP (Point to Point) Microwave – 50 miles+, 1Gbps+
    Satellite – Global, 100mbps*

## Slide 5: How does it work?
A RADIO’S PERFECT WORLD
  Clear line of site on a cool night
    Distance, Infrastructure, Weather, Foliage, Terrain, and RF Interference all effect performance.
    Lower Frequencies Propagate Better but have lower throughput
      Wi-Fi
        2.4ghz vs 5ghz
      Cellular
        4G (700mhz, 800mhz, 2300mhz)
        5G (low band <1ghz, mid band 1-6ghz, high band 24-40ghz)
        Higher Frequencies = more towers
  Fast Backhaul
    Preferably fiber
    Wireless backhaul (to fiber) can achieve 2Gbps+

## Slide 6: How does it work?
PATH INVESTIGATION

## Slide 7: How does it work?
PATH INVESTIGATION

## Slide 8: How does it work?
HEAT MAP

## Slide 9: How does it work?
RF SPECTRUM
  Spectrum is the range of electromagnetic radio frequencies used to transmit sound, data, and video across the country.
  Extremely valuable (100’s of Billions)
    FCC designates use across entire range
    Military, First Responders, Designated groups have priority
      Sold through auctions, Lobbied
  Licensed, Unlicensed, Light Licensed
    Licensed – Spectrum range is formally
    coordinated and strictly controlled.
    Interference is actively mitigated.
    Unlicensed – Anyone can use. Wi-Fi
    Lightly Licensed – Access is controlled
    but easily obtained

## Slide 10: How does it work?
RF SPECTRUM

## Slide 11: Why choose Wireless Broadband?
WIRELESS BENEFITS
  Cover large area with single site
  Usually cheaper than cabling to each location
  Faster deployment
    Fiber supply Issues
      1-4 Year timeline on fiber projects
  Do not need dedicated tower
    Water Towers
    Buildings
  Customer equipment is minimal

## Slide 12: Types of Wireless Broadband Networks
FIXED, MOBILE, SATELLITE
(25Mbps Download, 3Mbps Upload)
  Fixed Wireless – Both points fixed, nothing moves
    WISP
    Licensed and Unlicensed
    Easily deployable
  Mobile Wireless – At least one point is mobile
    Most Common (Cellular)
    Constantly upgraded
  Satellite – Only recently offered broadband speeds (Low Earth Orbit-Starlink)
    Most expensive
    Typically for very remote areas
    Very limited resources, not easily upgraded

## Slide 13: Wireless Broadband Around Town
Fixed Wireless CPE
Satellite Dish
FWA using Water Tower
Multiuse Tower

## Slide 14: NoaNet Wireless Broadband Deployment

## Slide 15: Wireless Broadband Architecture
FIXED WIRELESS ACCESS SCENARIO 1

## Slide 16: Wireless Broadband Architecture
FIXED WIRELESS ACCESS SCENARIO 2

## Slide 17: Wireless Broadband Networks
2.5 GHz
BRS/ EBS (Broadband Radio Service/ Educational Radio Service)
  Spectrum released from reserved but underused bands
  Sold via auction (all licensed)
    T Mobile primary incumbent
    Carriers pushing for another auction in 2022
  Tribal Priority Window
    Tribes could get priority access to spectrum
      Ended September 2020
    Current deployments in CCT and STOI
  Experience so far
    Excellent propagation through cover and non-los
    20 MHz = 110/12Mbps or 40 MHz = 220/24 using Carrier Aggregation

## Slide 18: Wireless Broadband Networks
3.5 Ghz
CBRS (Citizens Broadband Radio Service)
  Spectrum released from former Military spectrum
  150 MHz made available
    80 MHz available unlicensed
      7-10MHz blocks per county
  Three user tiers
    Incumbent, PAL (Prior Access License), GAA (General Authorized Access) i.e., ‘lightly licensed’
  Access controlled by FCC’s SAS (Spectrum Access System)
    Certified installer requests spectrum with SAS
      Each deployment registers with SAS to coordinate frequency
    System monitors spectrum via ESC (Environmental System Capability) onboard each device
    SAS operated by consortium (Federated Wireless, Google, CommScope, Amdocs, and Sony)
  NoaNet has test deployment in Tri-Cities

## Slide 19: Wireless Broadband Networks
3.5 GHz
CBRS (Citizens Broadband Radio Service)

## Slide 20: Wireless Broadband Networks
3.5 GHz
CBRS (Citizens Broadband Radio Service)

## Slide 21: The Persistently Unserved
WHAT ABOUT THE AREAS THAT ARE STILL UNSERVED OR UNDERSERVED?
Difficult terrain requiring trenching or boring can be cost prohibitive
Low population density to recoup the investment made through the sale of services makes investment not feasible
Subsidization will be required for the areas that are still unserved in our state. If there was a way to make it work without significant capital infusion, it would have happened by now!
IT’S NOT JUST ABOUT NETWORK
The Digital Divide is not a rural/urban issue- it is more complex
Affordability, access to technology and know-how can be as big of a barrier as lack of network availability.
We are in a time of unprecedented funding for broadband and communities across the state are stepping up!

## Slide 22: Thank you. Bring on the Questions! Sean Ogden & Greg Berry SOgden@noanet.net & Greg.Berry@noanet.net

## Slide 23: References
  RF Fundamentals
    Radio Transmission - https://www.youtube.com/watch?v=FWCN_uI5ygY&list=RDCMUCqZQJ4600a9wIfMPbYc60OQ&index=8&ab_channel=Lesics
    Modulation - https://www.youtube.com/watch?v=Iyzpt3bKTTI&ab_channel=Lesics
    Spectrum - https://www.youtube.com/watch?v=DXt-rXDu9M8&ab_channel=Lesics
  FCC Broadband Definition - https://www.fcc.gov/consumers/guides/broadband-speed-guide
  3.5 GHz - CBRS - https://www.celona.io/cbrs/what-is-cbrs
    Google SAS - https://www.google.com/get/spectrumdatabase/
  2.5 GHz - https://www.techdirt.com/articles/20201203/08111545814/fcc-25-ghz-spectrum-tribal- priority-window-something-positive-amid-covid-19-pandemic.shtml